## Slide 1: DEVELOPMENT OF A SYSTEM FOR FAST VIDEO DECODING IN AV1 FORMAT
Project proposal
performed by Ilya Bersenyov, ISD-22-2
Supervisor: V. V. Lanin

## Slide 2: Introduction
TAPe indexer is something like a one-way video encoder
Cause: TAPe average time to index is about 24 times faster than to decode a video
Effect: a large bottleneck in TAPe’s current pipeline
Goal: close the gap

## Slide 3: Relevance and hypothesis
Research aim is to design, implement and evaluate algorithmic optimisations for AV1 decoding at ultra-low output resolution in a single-threaded environment.
Hypothesis: Targeted algorithmic changes to the bottleneck stages of Libaom can reduce total system decoding time by 30–50 % while preserving acceptable video quality (PSNR ≥ 15 dB).
Object of study
libaom – the reference AV1 decoder
(spec v1.0.0 errata 1)
Subject of study
Decoding performance at 64 px output, single-threaded, no CUDA

## Slide 4: Research progress
Functional and non-functional requirements
Analysis of the AV1 Decoding specification
Identification of bottlenecks in the standard
Identification of all the methods to speed up the code
Choosing the technology stack
Designing the naive realization and the optimized realization
Implementing the realizations
Testing the realizations

## Slide 5: Theoretical background
The most resource-intensive components according to Chen et al. (2018):
Interpolation
Deblocking filter
Constrained directional enhancement filter

## Slide 6: Interpolation
Key point: it is very expensive.
8 coefficients 1d interpolation is the product of two vectors consisting of 8 numbers which is about 48 CPU cycles provided that multiplication takes 4 cycles and addition takes one cycle.

## Slide 7: DF (Deblocking Filter)
Key point: it is unnecessary in ultralow resolution.
DF is a method of reducing the blockiness of an image but is unnecessary in 64px resolution.

## Slide 8: CDEF (Constrained Directional Enhancement Filter)
Key point: it is too expensive operation.
CDEF is applied after the DF and is being used to make transitions between the canvas smoother.

## Slide 9: Lookup tables
Key point: it is faster than dynamic calculation but may lead to a lot of cache misses
Some values are “hard-coded” as arrays of values, where indexes are treated as function arguments.
Example:
double[] cos = {1.0,0.5,-0.4,-0.9,-0.7,0.2, …}; float x = cos[2];
Instead of
double x = cos(2)
However, as
Yi & Song (2008) state, excessive use may be harmful for the performance

## Slide 10: Methodological base
Replacing lookup tables with algebraic expressions (Yi & Song, 2008 — CAVLC for H.264): reduces memory footprint and eliminates cache misses on coefficient arrays.
Bitwise arithmetic optimization — "magic constant" division (Moroz & Samotyy, 2018): ≈30 % speedup on division-heavy interpolation paths.
Context-adaptive filter bypassing (Ren & Kehtarnavaz, 2007): skip costly post-processing steps when the target output is already ≤64 px.
Bentley optimisation rules + CPU-cache layout improvements: spatial locality in pixel buffers, prefetch-friendly access patterns.

## Slide 11: Metrics used
Total time from the upload to the end of the decoding process
Time to decode a video
A frame-by-frame metric estimated by the difference in brightness between each pixel of the original frame and the decoded one
Peak Signal-to-Noise Ratio (PSNR)
Stability and reproducibility of the obtained optimizations for Libaom, confirmed by at least five test runs with the same input data
Time to response in high load scenario
Compared to naive realization

## Slide 12: Plan of the practice part
Implementing the naïve realization
Implementing the optimized realization
  Lookup table
  Cache-optimized buffer pixel layout
  Analytic substitution (interpolation coefficients)
  Skip/simplify CDEF and DF at 64 or less px output
Evaluating the realizations

## Slide 13: Expected results
Total time to decode – 20-35% speed increasing
Time to decode – 30-50% speed increasing at minimum 5 runs
Confirmation of acceptable quality degradation
  PSNR ≥ 15Db
  Absence of critical artifacts affecting TAPe functionality

## Slide 14: Thank you for your attention
Introduction
Research progress
Theoretical background
Methodological base
Expected results